## Slide 1
Lecturer:
Simon Winberg
Digital Systems
EEE4084F
Lecture 19
Configuration architectures … & other
FPGA-based RC Building Blocks

## Slide 2: Lecture Overview
Configuration architectures
Short video on NIOS II
RC Building blocks
  Memories
  DMA
  Digital Signals
  Signal Latching

## Slide 3: Configuration Architectures
RC Architecture

## Slide 4: Configuration Architectures
Configuration architecture =
  Underlying circuitry that loads configuration data and keeps it at the correct locations
CPU
Finite State Machine
ROM
Configuration
controller
FPGA
Configuration
data
Configuration
control
Configuration
requests
Adapted from Hauck and Dehon Ch4 (2008)
Could store pre-configured bitmaps in memory
on the platform without having to send it each time
from the CPU. Include hardware for programming
the hardware (instead of the slower process of e.g.,
programming devices via JTAG from the host)

## Slide 5: Configuration Architectures
Larger systems (e.g., the VCC) may have many FPGAs to be programmed)
Models:
  Sequentially programming FPGAs by shifting in data
  Multi-context – having a MUX choose which FPGA to program
Adapted from Hauck and Dehon Ch4 (2008)
Configuration
bit
…
FPGA
FPGA
FPGA
Configuration
clock
Configuration
enable
IN
OUT
IN
OUT
IN
OUT

## Slide 6: Configuration Architectures
Partially reconfigurable systems
  Not all configurations may need entire chip
  Could leave parts of chips unallocated
  Partial configuration decreases configuration time
  Modifying part of a previously configured system
    E.g., a placement and routing configuration based on a currently configured state
Initial Configuration
Updated Configuration

## Slide 7: Configuration Architectures
Block configurable architecture
  Not the same as “logical blocks” in an FPGA
  Relocating configurations to different blocks at run time also referred to as “swappable logic units” (SLUs)
Example: SCORE* relocatable architecture in which configurable blocks are handled in the same way as a virtual memory system
* Capsi & DeHon and Wawrzynek. “A streaming multithreaded model” In Third workshop on media and stream processors. 2001

## Slide 8: Additional Reading
Reading
  Hauck, Scott (1998). “The Roles of FPGAs in Reprogrammable Systems” In Proceedings of the IEEE. 86(4) pp. 615-639.

## Slide 9
Short Video…
Towards mobile augmented reality…
Computer Vision Accelerator.wmv

## Slide 10: Memory types
Volatile
Non-volatile

## Slide 11: Volatile memory
DRAM
  Capacitor stores “memory” that leaks away and needs to be periodically refreshed
  High memory capacity
SDRAM = Synchronous DRAM
  Runs in synch with system* clock
  DDR SDRAM = Double-data rate SDRAM, runs at 2x the system clock
* Note the system clock in this case is closer to the “motherboard” clock. Usually considerably slower than the processor clock (standard DRAM may have its own even slower clock and synchronization hassles)

## Slide 12: Volatile memory
SRAM
  Static RAM
  Does not need refreshing
  Uses “bistable latching circuitry” (i.e. a flip flop) to store each bit
  Can be very fast compared to DRAM
  A small amount of SRAM (~16 Kb) is typically used within a microcontroller / FPGA to hold things such as a boot loader and interrupt vectors, and as CACHE
SR Latch to hold
a bit of SRAM *
SR Latch implemented using two NOR gates *
* Images from http://en.wikipedia.org/wiki/Latch_(electronics)

## Slide 13: Volatile Memory
BRAM or Block RAM
  This refers to a small block of RAM (a few Kilobytes) integrated within the FPGA (connected some LBs)
  Generally only found in higher-end FPGAs (e.g. 16Kb takes ~ 256K transistors if not more for connection and addressing logic)
  Block SRAM is more common and easier to use; the FPGA may include Block DRAM
  Generally can be set to RAM or ROM
  As ROM it can be used as a (big) LUT
  Usually not directly accessible form outside the FPGA (need to provide circuitry / softcore and comms protocol to access it from a PC)

## Slide 14: Volatile memory
Under development
  Z-RAM : Zero-capacitor RAM
    Single transistor
    Higher density than DRAM
    Although it is called zero-capacitor, the capacitor is actually there in the form of a “floating body effect” caused by the transistor substrate
    See: http://www.innovativesilicon.com/

## Slide 15: Non-Volatile memory
Trusty old ROM and EEPROM
  Still widely used as it is highly robust
  Current versions store large amounts of data
  Fairly simple technology (i.e. fused connections) and (in EEPROM ability to fuse and then program/un-fuse connections)
Usually ROM is slower than RAM
Shadowing ROM (i.e. copy to RAM) to make it faster – especially for EEPROMs
EEPROM very slow write; faster read

## Slide 16: Non-Volatile Memory
Flash memory
  Can be electrically erased and programmed
  High capacity (e.g., millions of bytes/chip)
  Needs to be programmed one block at a time (~8Kb / block)
    Erased (all bits in block set to 1)
    Programmed one block at a time
  Memory wear
    Limited to about 100,000 erase – write cycles
    Usually a file system (e.g. ext3) will keep track of bad sectors (i.e., mark deteriorated blocks). But this deterioration might happen a certain time after the erase and write is complete and verified.

## Slide 17: NAND Flash memory model
The above diagram provides a macro circuit model for a single flash memory cell, showing a Effective-Control-Gate (ECG) equivalent circuit and the Ideal-Current-Mirror (ICM) used to calculate the floating gate (FG*) voltage. MOSFET1 is the equivalent N-MOSFET model of a flash memory cell, and MOSFET2 is the model of a N-MOSFET test structure that is identical with the flash memory cell (excluding the short between FG and CG).
*
Image source: IEEE Electron Device Letters, Vol. 26, No. 8, AUGUST 2005, pg 564 Available at: http://koasas.kaist.ac.kr/bitstream/10203/1570/1/01468223.pdf

## Slide 18: RC Building Blocks: Digital Signals and Data Transfers
Reconfigurable Computing

## Slide 19: Overview of digital signals
Although our objective is towards parallel operations, there are still sequential issues involved, for example a device B waiting for a device A to provide input
Furthermore the input to a device A might disappear (become invalid) before device A has completed its computations.
In
Out
Device A
Device B

## Slide 20: Overview of digital signals
There are other issues involved such as:
  How does device A know when new data has arrived?
  How does device B know when device A has completed?
  What if both devices need to be clocked, but aren’t active all the time?
  What if you want to share address and data lines?
In
Out
Device A
Device B
handshaking
lines

## Slide 21: Digital logic modular design issues
OUTPUTS
A sequential logic system typically involves two parts:
  Storage (aka “bistable” device)
  Combinational logic (OR, AND, etc gates)
INPUTS
Combinational Logic Device
Storage
Data
Data
Another
combinational logic device(s)
Another
combinational logic device(s)
potentially shared data busses, possibly 2 separate busses for full-duplex, one for read one for write
control lines (e.g., do you want to read or write, are you done setting all the bits, etc.)

## Slide 22: Digital Signals
Usually need the following
  Address bus
  Data bus
  Control lines
    Chip / Device select lines
    Write enable lines
    Read enable lines

## Slide 23: RC Building Blocks: DMA – Efficient Data Transfer
Reconfigurable Computing

## Slide 24: Direct Memory Access (DMA)
Originally direct memory access (DMA) referred to a feature provided on a computer systems whereby peripherals within the computer can access the system memory for reading and/or writing independently of the central processing unit.
This is still an appropriate definition; except rather consider DMA as a more general description, whereby separate hardware can both access memory directly (without the CPU doing any work), and can request the memory subsystem (really the DMAC) to perform memory copies or transfers.

## Slide 25: Typical computer design without DMA
address
Address Decoder
Memory (Device 0)
address
CS0*
CS*
UART
(Device 1)
CS1*
CS2*
CS*
RD*
…
RD*
CPU
WR*
WR*
data
data
Signals:
Address : address line (e.g. 32 bits)
Data : data line (e.g., 32 bits)
IRQ : Interrupt ReQuest line
CS* : Chip select (active low)
RD* : Read enable (active low)
WR*: Write enable (active low)
IRQ
IRQ
In this approach, each peripheral
signals the CPU and tells it to
receive data and r/w memory

## Slide 26: DMA : Direct Memory Access
address
Memory
CPU
IRQ
DMA Direct memory access is system in which memory is accessed without using the CPU. A certain stimulus (e.g. a device needing data sent/received) can have this data sent/received directly from/to a block of memory location via the DMA controller (DMAC). Peripherals such as ADCs, GPUs and Ethernet, which require frequent movements of memory, typically support DMA. DMA controllers can be configured to handle moving collected data from peripherals into specific memory locations (e.g., arrays directly accessible from a C program). Additional control logic is required to manage the sharing of the address and data bus.
IRQ
Further reading: http://www.freebsd.org/doc/en/books/developers-handbook/dma.html
data
Device
(e.g., Graphics Card)
DMA
Controller

## Slide 27: DMA configurations
Standard block transfer
  DMAC does sequence of memory transfers
  Load operation from source address, store operation to destination
  Initiated under software control (e.g., copying data from one memory area to another) i.e., array X = array Y
Demand-mode transfer
  Same as block transfer, but controlled by external device. I/O device requests and synchronizes the operation
Ref: Catsoulis, J. (2003). Designing Embedded Hardware. O’Reilly.

## Slide 28: DMA configurations
Fly-by transfers
  High speed operation
  Memory and I/O on different bus
  E.g., I/O given read request at same time that memory is given write request
  Can simultaneously read/write I/O device and write/read memory
Data-chaining transfers
  Linked list in memory
  DMAC given pointer to descriptor
  Descriptor indicates: size, src address, dest address, next descriptor

## Slide 29: DMAC Modes of Operation
Adapted from source: http://calab.kaist.ac.kr
Byte Mode
Burst Mode
DMA Controller can support a range of modes. The three modes shown left are commonly supported.
Block Transfer Mode
123w123w123w…
1
2
3
w
1
2
w
3
12w2w2w3…
12w2w2www…
1
2
w
Sequence of states
CPU deactivates

## Slide 30: RC Building Blocks: Latching (capturing Signals)
Reconfigurable Computing

## Slide 31: Digital Signal Capture and Storage
In order to capture the signals, you need some storage
Two basic types of storage:
Latches
Flip-flops

## Slide 32: Difference between latch and flip-flop
Latches Q = D
  Changes state when the input states change (referred to as “transparency”)
  Can include an enable input bit – in which case the output (Q) is set to D only when the enable input is set.
Flip-flop Q = D (Q changes when clocked)
  A flip-flop only change state when the clock is pulsed.

## Slide 33: When to use a latch or a flip-flop
Latches are used more in asynchronous designs
Flip-flips are used in synchronous designs
A “synchronous design” is a system that contains a clock
You can of course mix synchronous and asynchronous, and this is particularly applicable to parallel systems in which different parts of the system may run at different speeds (e.g., the main processor working at 1GHz and specialized hardware possibly operating asynchronously as fast as their composite pipelined operations are able to complete)

## Slide 34: SR Latch
A | B | X | Y
0 | 0 | 1 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 1 | X | X
A basic latch has two stable states:
State 1 Q = 1 not Q = 0
State 2 Q = 0 not Q = 1
And an unstable state in which both S and R are set (which can
cause the Q and not Q lines to toggle)
S-R Latch (set / reset latch)
Symbol

## Slide 35: Gated SR Latch: a latch with enable
Combinational logic circuit with a clock (or enable) input connected
Usually the type used in digital systems.
It of course costs more in transistors!!
Example signals
or “gate” input
Only changed on clock pulse
Gated SR-Latch
Symbol

## Slide 36: Flip-flop
The standard JK flip-flop is much the same as a gated SR latch, modified so that Q toggles when J = K = 1
The D-type flip flop (which you may want to use in Prac3 to store data) is a JK flop flop modified (see left) to hold the state of input D at each clock pulse.
JK flip-flop
D flip-flop
clock | D | Q
0 | 0 | X
1 | 1 | 0
2 | 1 | 1
3 | 0 | 1
… | … | …

## Slide 37: T-type Flip-flop
The T-type flip-flops toggle the input. Q = not Q each time T is set to 1 when the clock pulses
The D-type flip flop (which you may want to use in Prac3 to store data) is a JK flop flop modified (see left) to hold the state of input D at each clock pulse.
T flip-flop
D flip-flop
Clock | T | Q
0 | 1 | 0
1 | 0 | 1
2 | 1 | 1
3 | 0 | 0
… | … | …

## Slide 38: Preset and Clocking
Preset line (PR) and clear line (CL) are asynchronous inputs used to set (to 1) or clear the value stored by the flip-flop.

## Slide 39: Edge triggered devices
A note on notation:
Edge-triggered inputs are shown using a triangle.
Negative edges triggered inputs are shown without a circle on the incoming line.
in
Negative edge triggered
in
Positive edge triggered

## Slide 40: End of Lecture
Any Question??