## Slide 1
Lecture 7:
Parallel Computing Fundamentals
Presented by
Simon Winberg
High Performance
Embedded Systems
EEE4120F
Attribution-ShareAlike 4.0 International (CC BY-SA 4.0)
Planned to be double period lecture

## Slide 2: Lecture Overview
Parallel Computing Fundamentals
Large Scale Parallelism
Mainstream parallel
Classic Parallel approaches
Flynn’s Taxonomy
Some Calculations
  Effective parallelism
  Parallel Efficiency
  Gustafson’s Law

## Slide 3: Parallel Systems
EEE4120F: Digital Systems
A?
B?
C?
+
*
X !
Y !
-
Remember the spatial computing paradigm??

## Slide 4: Computation Methods
Hardware
Reconfigurable
Computer
Software
Processor
e.g. PCBs, ASICs
Advantages:
High speed & performance
Efficient (possibly lower power than idle processors)
Parallelizable
Drawbacks:
Expensive
Static (cannot change)
e.g. IBM Blade, FPGA-based
computing platform
Advantages:
Faster than software alone
More flexible than software
More flexible than hardware
Parallelizable
Drawbacks:
Expensive
Complex
(both s/w
& h/w)
e.g. PC, embedded software on microcontroller
Advantages:
Flexible
Adaptable
Can be much cheaper
Drawbacks:
The hardware is static
Limit of clock speed
Sequential
processing
this term
Reminder …

## Slide 5: Mainstream parallel computing
Most server class machines today are:
  PC class SMP’s (Symmetric Multi-Processors *)
  2, 4, 8 processors - cheap
  Run Windows & Linux
Delux SMP’s
  8 to 64 processors
  Expensive:
  16-way SMP costs ≈ 4 x 4-way SMPs
Applications: Databases, web servers, internet commerce / OLTP (online transaction processing)
Newer applications: technical computing, threat analysis, credit card fraud...
SMP offers all processors and memory on a common front side bus (FSB –bus that connects the CPU and motherboard subsystems).
* Also termed “Shared Memory Processor” (but you might get 0 for giving this alternate term in a test)

## Slide 6: Large scale parallel computing systems
Hundreds of processors, typically as SMPs clusters
Traditionally
  Often custom built with government funding (costly! 10 to 100 million USD)
    National / international resource
    Total sales tiny fraction of PC server sales
  Few independent software developers
  Programmed by small set of majorly smart people
Later trends
  Cloud systems
  Users from all over
  E.g. Amazon EC, Microsoft Azure

## Slide 7: Large scale parallel computing systems
Some application examples
  Code breaking (CIA, FBI)
  Weather and climate modeling / prediction
  Pharmaceutical – drug simulation, DNA modeling and drug design
  Scientific research (e.g., astronomy, SETI)
  Defense and weapons development
Large-scale parallel systems are often used for modelling

## Slide 8: Digital Accelerators: New Practice
HP Intel 5110P Xeon Phi Coprocessor Kit
Intel Xeon Phi
Where and why it’s no longer being made, replaced by Xeon Scalable Platform
  And… some of this it may involve designing specialized compute architectures for the need (using a combination of languages and tools e.g. OpenCL / Verilog, C, R, etc.)
Digital accelerator cards (including GPGPUs) are increasing in popularity, including in data centres.
Xilinx Alevo: Adaptable Accelerator Cards for Data Centres
https://www.xilinx.com/products/boards-and-kits/alveo.html
Program with OpenCL or Xilinx’s owns accelerator design suite.
Intel Ice Lake
(10 nm process) 10th generation core, successor for Xeon Phis.
Core i7 1068G7 (2020 debut) 4 CPU cores + 64 Iris+ GPCPU cores
Replaced by (from 2020)
  (launched end 2018)
  (ended 2019)
* What was it said in the “Berkeley Landscape” … “Small is beautiful” and “manycore is the future of Computing”.
Term 2: RC / Digital Accelerators

## Slide 9: Classic Parallel
EEE4120F

## Slide 10: Classic techniques for parallel programming*
Single Program Multiple Data (SPMD)
  Consider it as running the same program, on different data inputs, on different computers (possibly) at the same time
Multiple Program Multiple Data (MPMD)
  Consider this one as running the same program with different parameters settings, or recompiling the same code with different sections of code included (e.g., uisng #ifdef and #endif to do this)
Following this approach performance statistics can be gathered (without necessarily any parallel code being written) and then evaluated after the effect to deem the feasibility of implementing a parallel (e.g. actual pthreads version) of the program.
*Informally know as the lazy parallel programming model.
NB: Class Activity A
Can consider the SPSD (i.e. Single Program Single Data) as the case where the whole program is run once on all the data.
Notes: Class activity A handout: context of simply program scenario that you want to have a basic parallel golden measure. It simply find min, max and average of a dataset. Then pose a SPMD approach, an MPMD approach and see to what extent either of these are better or worse then just the basic golden measure run on the whole block of data.

## Slide 11: Terms
EEE4120F

## Slide 12: Terms (reminders)
Observed speedup =
Parallel overhead:
  Amount of time to coordinate parallel tasks (excludes time doing useful work).
  Parallel overhead includes operations such as: Task/co-processor start-up time, Synchronizations, communications, parallelization libraries (e.g., OpenMP, Pthreads.so), tools, operating system, task termination and clean-up time
Wallclock time initial version
Wallclock time refined version
Wallclock time sequential (or gold)
Wallclock time parallel version
=
The parallel overhead of the lazy parallel model could clearly be extreme, considering that is would rely on manual intervention to (e.g.) partition and prepare the data before the program runs.

## Slide 13: Some terms
Embarrassingly Parallel
  Simultaneously performing many similar, independent tasks, with little to no coordination between tasks.
Massively Parallel
  Hardware that has very many processors (execution of parallel tasks). Can consider this classification of 100 000+ parallel tasks.
{ Stupidly Parallel }
  While this isn’t really an official term it typically relates to instances where a big (and possibly very complex) coding effort is put into developing a solution that in practice has negligible savings or worse is a whole lot slower (and possibly more erroneous/buggy) than if it was just left as a simpler sequential implementation.

## Slide 14
Using scalar product pthreads type implementation for scenarios…
Introducing to some important terms related to shared memory
Notes: The following slides introduce important terms that are used commonly to refer to memory partitioning methods. Each of these terms, besides contiguous – since that is no partitioning - can be refined further depending on the problem and the way that data is being stored or managed.

## Slide 15: Partitioned memory
[a1 a2 a1 a2 … am-1]
[b1 b2 b1 b2 … bm-1]
Thread 1
sum1
Vectors in
global / shared
memory
[am am+1 am+2 … an]
[bm bm+1 bm+2 … bn]
Thread 2
sum2
starts
main()
sum = sum1+sum2
Assuming a 2-core machine
1
1
2
2
a
b
main()
Memory access by thread

## Slide 16: Interlaced* memory
[a1 a3 a5 a7 … an-2]
[b1 b3 b5 b7 … bn-2]
Thread 1
sum1
Vectors in
global / shared
memory
[a2 a4 a6 … an-1]
[b2 b4 b6 … bn-1]
Thread 2
sum2
starts
main()
sum = sum1+sum2
Assuming a 2 core machine
a
b
* ‘Data striping’, ‘interleaving’ and ‘interlacing’ usually means the same thing but not always.
See further explanation between these on: https://wikidiff.com/interleave/interlace
main()
Memory access by thread
NB: benefits of interleaving as a means to improve robustness and access of memory
interlacing vs. interleaving : see comments
Notes: The aspect of interlaced and interleaving of memory connects also with aspects of data transfer, sampling, and communication.
Interlaced : to cross one another, like weaving e.g. /\/\/\ + \/\/\/ = XXXXX
“to cross one with another; to interweave: as, to interlace wires; hence, to mingle; to blend.” (source: https://wikidiff.com/interleave/interlace)
Interleaved : to insert between or separate at regular intervals, or data that is for different purposes. E.g. instead of sending ‘hello’ and the sequence ‘12345’ as separate messages, for potentially different purposes, e.g. the one an ping response and the other result of a calculation, the data could be interleaved as h1e2l3l4o5. The receiving system would need to know how to make use of the interleaved data and potentially separate back into its constituent parts.

## Slide 17: Memory Partitioning Terms
Contiguous
Partitioned (or separated or split)
Interleaved/interlaced (or alternating or data striping)
Interleaved – large strides (e.g. row of image pixels at a time)
Interleaved – small stride (e.g. one word stride)
(the ‘stride’ in data interleaving or data striping refers to the size of the blocks alternated, generally
this is fixed but could be changeable, e.g. the last stride might be smaller to avoid padding data.)
SUMMARY

## Slide 18: Flynns Taxonomy of Processor Architectures
EEE4120F
Type
A
Type
B
Type
C
Type
D
Type
E
Type
F
Type
G
Type
H
Type
I
Type
J

## Slide 19: Flynn’s taxonomy
Flynn’s (1966) taxonomy was developed as a means to classify parallel computer architectures
Computer system can be fit into one of the following four forms:
SISD
Single Instruction Single Data
SIMD
Single Instruction Multiple Data
MISD
Multiple Instructions Single Data
MIMD
Multiple Instructions Multiple Data
Not to be confused with the terms of “Single Program Multiple Data (SPMD)” and “Multiple Program Multiple Data (MPMD)” mentioned earlier.
Flynn’s
Taxon.
MI
MD

## Slide 20: Single Instruction Single Data (SISD)
This is (obviously) the classic von Neumann Computer: serial (not parallel) computer, e.g.:
  Old style single core PC CPUs, e.g. i486
Single instruction 
  One instruction stream acted on by the CPU during any one clock cycle
Single data 
  Only one input data stream for any one clock cycle
Deterministic execution
0x1000
LD A,[0x2002]
0x1003
LD B,[0x2004]
0x1006
ADD A,B
0x1007
SHL A,1
0x1008
ST A,[0x2000]
x = 2 * (y + z);

## Slide 21: Single Instruction Multiple Data (SIMD)
A form of parallel computer
  Early supercomputers used this model first
  Nowadays it has become common – e.g., used in modern computers on GPUs
Single instruction 
  All processing units execute the same instruction for any given clock cycle
Multiple data 
  Each processing unit can operate on a different data element
LD AX,[DX+0]
LD BX,[EX+0]
ADD AX,BX
SHL AX,1
ST AX,[CX+0]
y= [1 2 3 4]
z = [2 3 4 5]
x = 2 * (y + z)
…
LD AX,[DX+3]
LD BX,[EX+3]
ADD AX,BX
SHL AX,1
ST AX,[CX+3]
…
…
CPU 1
CPU 4

## Slide 22: Single Instruction Multiple Data (SIMD)
Runs in lockstep (i.e., all elements synchronized)
Works well for algorithms with a lot of regularity; e.g. graphics processing.
Two main types:
  Processor arrays
  Vector pipelines
Still highly deterministic (know the same operation is applied to specific set of data – but more data to keep track of per instruction)

## Slide 23: Single Instruction Multiple Data (SIMD) Examples
Vector pipelines
  IBM 9000, Cray X-MP, Fujitsu vector processor, NEC SX-2, Hitachi S820, ETA10
Processor arrays
  Thinking Machine CM2, MasPar MP-1 & MP-2, ILLIAC IV
Graphics processor units usually use SIMD
Cray X-MP
MasPar MP-1

## Slide 24: Multiple Instruction Single Data (MISD)
Single data stream fed into multiple processing units
Each processing unit works on data independently via independent instruction streams
Few actual examples of this class of parallel computer have ever existed

## Slide 25: Multiple Instruction Single Data (MISD) Example
…
…
…
Possible uses? Somewhat intellectual?
  Maybe redundant! (see next slide)
Possible example application:
  Different set of signal processing operations working the same signal stream
x = +MAXINT
Example:
Simultaneously find the min and max input, and do a sum of inputs.
x = -MAXINT
x = 0
If A<x then x = A
If A>x then x = A
x = x + A
A = input
CPU 1
CPU 2
CPU 3

## Slide 26: Multiple Instruction Multiple Data (MIMD)
The most common type of parallel computer (most late model computers, e.g. Intel Core Duo, in this category)
Multiple Instruction 
  Each processor can be executing a different instruction stream
Multiple Data 
  Every processor may be working with a different data stream
Execution can be asynchronous or synchronous; non-deterministic or deterministic

## Slide 27: Multiple Instruction Multiple Data (MIMD)
Examples
  Many of the current supercomputers
  Networked parallel computer clusters
  SMP computers
  multi-core PCs
MIMD architectures could include all the other models. e.g.,
  SISD – just one CPU active, others running NOP
  SIMD – all CPUs load the same instruction but apply to different data
  MISD – all CPUs load different instructions but apply it to the same data
AMD Opteron
IBM BlueGene

## Slide 28: Maximum Effective Parallelism
EEE4120F

## Slide 29
Significant Tradeoff:
Infrastructure & Setup Cost
vs.
Effective Parallelism
Consideration for
- hardware
- software
Maximum Effective Parallelism:
This refers to the point of the number of cores / amount of parallelism beyond which additional parallelism provides no further benefit or (worse) may reduce performance.
go parallel!

## Slide 30
Significant Tradeoff:
Infrastructure & Setup Cost
vs.
Effective Parallelism
Maximum Effective Parallelism:
This refers to the point of the number of cores / amount of parallelism beyond which additional parallelism provides no further benefit or (worse) may reduce performance.
cores / available parallelism
Performance
improvement
(speedup)
cores / available parallelism
cost of parallelism
cores / available parallelism
startup time
Hardware
Software
cores / available parallelism
comms cost and time

## Slide 31: Calculation Example: Maximum Effective Parallelism
Remember from Amdahl:
  S = TS / TP (i.e. sequential time over parallel time)
You can use these equations to approximate behaviour of modelled systems.
E.g.: to represent speedup, comms overhead, cost of equipment, etc. and use calculations to estimate optimal selections. (simple example to follow)

## Slide 32: Learning Activity
Quick estimation for maximum effective parallelism
Solution follows shortly!
Please try it for your self, or work with a buddy to think about how to respond to this question.

## Slide 33: Learning Activity Answer
N | Proc (ms) | Comms (ms) | Total (ms)
1 | 100.000 | 0 | 100.000
2 | 50.000 | 10 | 60.000
4 | 25.000 | 20 | 45.000
8 | 12.500 | 40 | 52.500
16 | 6.250 | 80 | 86.250
32 | 3.125 | 160 | 163.125
64 | 1.563 | 320 | 321.563
Could do some rough calculations (or use binary search)…
check:
N=2,
N=64,
N=8,
N=4 

## Slide 34: Multi processors and sequential setup time
2nd part of Amdahl’s law video
Amdahl2.flv
Understanding Parallel Computing (Part 2): The Lawn Mower Law LinuxMagazine
If you haven’t already watched this please do!

## Slide 35: Parallel Efficiency (Epar)
We can think of the efficiency of various things, e.g. power systems, motors, heaters etc. We can also think of the efficiency of parallel computing…
Parallel Efficiency
  Defined as the:
ratio of speedup (S) to the number of processors (p)
  Parallel Efficiency measures the fraction of time for which a processor is usefully used.
  An efficiency of 1 is ideal (>1 means you may be harnessing energy from another dimension )

## Slide 36: Parallel Efficiency (Epar)
Sp
p (number cores)
sub-linear speedup
linear speedup
super-linear
speedup
(awesome!)
Parallel Efficiency
p = number processors
Ts = exe time of the seq. alg.
Tp = exe time of the parallel alg. with p processors used
Sp= speedup (linear being the realistic ideal)

## Slide 37: Gustafson’s Law *
Gustafson's law =
  The theoretical speedup in latency of the execution of a task at fixed execution time that can be expected of a system whose resources are improved.
  A follow-up to Amdahl's Law
* also referred to, more fairly, as the Gustafson–Barsis's law
Speedup S gained by N processors (instead of just one) for a task with a serial fraction s (not benefiting from parallelism) is as follows:
formulation:
S = speedup, N = cores, s = serial portion
Using different variables, can be formulated as:
Slatecy = theoretical speedup in latency of the execution of the whole task
p = % of workload before the improvement that will be speeded up.
s = speedup in latency of part of the task benefiting from improved parallelism

## Slide 38: Gustafson’s Law
This is a plot of
s going from 0.5 to 2
p going from 10% to 100%
As you can see, the latency is reduced (i.e. Slatency increased) as s increases and p increases.
But for e.g. a real speedup of 2 you actually need p=100% (i.e. the entire workload improved) to achieve it.
Chart: Speedup in Latency (Slatency)
| 0.1 | 0.2 | 0.30000000000000004 | 0.4 | 0.5 | 0.6 | 0.7 | 0.79999999999999993 | 0.89999999999999991 | 0.99999999999999989
Sl_0.25 | 0.925 | 0.85 | 0.775 | 0.7 | 0.625 | 0.55 | 0.475 | 0.4 | 0.325 | 0.25
Sl_0.50 | 0.95 | 0.9 | 0.85 | 0.8 | 0.75 | 0.7 | 0.65 | 0.6 | 0.55 | 0.5
Sl_1.00 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Sl_1.25 | 1.025 | 1.05 | 1.075 | 1.1 | 1.125 | 1.15 | 1.175 | 1.2 | 1.225 | 1.25
Sl_1.50 | 1.05 | 1.1 | 1.15 | 1.2 | 1.25 | 1.3 | 1.35 | 1.4 | 1.45 | 1.5
Sl_2.00 | 1.1 | 1.2 | 1.3 | 1.4 | 1.5 | 1.6 | 1.7 | 1.8 | 1.9 | 2
s = 2
s = 1.5
s = 1.25
s = 1
s = 0.5
s = 0.25
p = % of workload before the improvement that will be speeded up.
s = speedup in latency of part of the task benefiting from improved parallelism
Gustafson’s law can be more useful to real-time embedded systems because it look more towards improving the response time of a system.

## Slide 39
Glimpse into Next Lecture
Amdahl’s Law Revisited:
The next lecture helps you understand the prescribed reading, a highly influential paper, that brings Amdahl’s Law more accurately into the 21st century.
Applying refinements for the heterogeneous, multicore era of computing….

## Slide 40
End of Lecture
FREE Creative Commons License
COUNTRY BOY
Music: https://www.bensound.com

## Slide 41
Image sources:
Clipart sources – public domain CC0 (http://pixabay.com/)
PxFuel – CC0 (https://www.pxfuel.com/)
FreeSVG – CC0 public dimain images (https://freesvg.org/)
Pixabay
commons.wikimedia.org
Images from flickr
Disclaimers and copyright/licensing details
I have tried to follow the correct practices concerning copyright and licensing of material, particularly image sources that have been used in this presentation. I have put much effort into trying to make this material open access so that it can be of benefit to others in their teaching and learning practice. Any mistakes or omissions with regards to these issues I will correct when notified. To the best of my understanding the material in these slides can be shared according to the Creative Commons “Attribution-ShareAlike 4.0 International (CC BY-SA 4.0)” license, and that is why I selected that license to apply to this presentation (it’s not because I particulate want my slides referenced but more to acknowledge the sources and generosity of others who have provided free material such as the images I have used).