## Slide 1
Lecture 10:
Design of
Parallel Systems
Presented by
Simon Winberg
High Performance
Embedded Systems
EEE4120F
Attribution-ShareAlike 4.0 International (CC BY-SA 4.0)
PART 2/3

## Slide 2: Steps in Designing Parallel Programs
Continuing the path to HPES Applications
Hardcore competent HPES programmers
(leading the way to greater feats)
Sequential programmers in their comfort zone.
EEE4120F
Hey, guys!
I forgot my warm jacket, can we go back??

## Slide 3: The steps in designing parallel programs
…
The hardware may be done first… or later.
The main steps:
Understand the problem
Partitioning (separation into main tasks)
Granularity
Communications
Identify data dependencies
Synchronization
Load balancing
Performance analysis and tuning
this lecture
PART 2/3
next week

## Slide 4: Lecture Overview
Step 6: Synchronization
Step 7: Load balancing
Step 8: Performance analysis and tuning

## Slide 5: Steps in designing parallel programs
The hardware may come first or later
The main steps:
Understand the problem
Partitioning (separation into main tasks)
Decomposition & Granularity
Communications
Identify data dependencies
Synchronization
Load balancing
Performance analysis and tuning
later

## Slide 6: Step 6: Synchronization
EEE4120F
Design of Parallel Programs

## Slide 7: Types of Synchronization
Barrier
Locking / Semaphores
Synchronous communication operations

## Slide 8: Barrier
All tasks are involved
Each task does work until it reaches the barrier, and then blocks.
When the last task reaches the barrier all the tasks are synchronized.
What happens next?…
  Section of work is done or
  Tasks are automatically released to continue their work… programmer usually decides.

## Slide 9: Locking / Semaphores
May concern any number of tasks
Usually used to serialize / protect access to global data or critical section of code.
Only one task at a time may have the lock / semaphore.
Tasks can attempt to get the lock need to wait for the task that has the lock to release it, granted on a FCFS basis.
Usually blocking, could be non-blocking (i.e., do other work until lock is available)

## Slide 10: Synchronous communication operations
Concerns only tasks executing a communication operation (or comms op)
When a task performs a comms op, some form of coordination is required with other task(s) involved with this communication.
  For example, before a task can do a send operation, it needs to first receive a clear to send (CTS) signal from the task it wants to send to.

## Slide 11: Step 7: Load Balancing
EEE4120F

## Slide 12: Load Balancing
Distributing work among tasks so that all tasks are kept busy most of the time
Mainly a minimization of idle time
Relevant to parallel programs for optimizing performance.
  e.g., if every tasks encounters a barrier synchronization point, the slowest task will end up limiting the overall performance.
Relevant to costing, e.g. deciding number of processors needed (can also be used in substantiating the need for a more, rather than less, expensive platform)

## Slide 13: Load Balancing – simple trial technique
…
typedef struct { unsigned start, end; } LogEntry;
LogEntry logt[1024];
int logn = 0;
unsigned prog_start, prog_end;
void* task (void* arg)
{
unsigned int end;
unsigned int start = clock();
// do work
// calculate time it took
end = clock();
// update time log
pthread_mutex_lock(&mutex);
logt[logn].start = start; logt[logn].end = end; logn++;
pthread_mutex_unlock(&mutex);
}
idle
busy
… in main() get prog_start time, create mutex & threads, wait join, get prog_end time.
prog_start
prog_end
logt[0].start
logt[1].end
logt[1].start
logt[0].end

## Slide 14: Load Balancing – simple trial technique (cont)
...
double calc_stat_stddev ()
{ // calculate standard deviation of busy times
int i;
double sum = 0;
for(i = 0; i < logn; i++) sum += logt[i].end - logt[i].start;
double mean = sum / logn;
double sq_diff_sum = 0;
for(i = 0; i < logn; ++i) {
double diff = logt[i].end - logt[i].start - mean;
sq_diff_sum += diff * diff;
}
double variance = (double)sq_diff_sum / logn;
return sqrt(variance);
}
…

## Slide 15: Load Balancing
Task 1
Time idle
time busy
Task 2
Time idle
time busy
Task 3
Time idle
time busy
Task 4
Time idle
time busy
Well balanced – low standard deviation in busy time*
Overall
Time idle
time busy
time busy
Time idle
busy
Time idle
time busy
Time idle
busy
Overall
Time idle
time busy
Poorly balanced – high standard deviation in busy time
* You could obviously use idle time – but that’s probably more difficult if using code in prev. slide
Task 1
Task 2
Task 3
Task 4

## Slide 16: Achieving load balance
Two general techniques…
Equally partition work as a preprocess
  Workload can be determined accurately before starting the operation
Dynamic work assignment
  For operations where the workload is unknown, or cannot be effectively calculated, before starting the operation

## Slide 17: Achieving balance – Work assignment as pre-process
Examples include
  Array or matrix operations for which each task performs similar work. Can evenly distribute the data set among tasks / available processors.
  Loop iterations where the work in each iteration is similar, and can be evenly distributed.
May be less easy to do if using a heterogeneous mix of machines that have varying performance characteristics. In such cases, a comprehensive analysis tool may be needed to determine load imbalances and revise work disctribution.

## Slide 18: Achieving balance – Work assigned dynamically
Examples include
  Sparse arrays/matrices (i.e., if matrix simply divided equally, some tasks may have lots to do but others little to do)
  N-body simulations (particles owned by some tasks may involve more work than others)
  Adaptive grid refinement (some tasks may need to refine their grips)
General principle: tasks that are busier send a request for assistance, whereas tasks that complete quickly are available to help the busier tasks.

## Slide 19: Vertical vs. horizontal load balancing
Load Balancing with Cloud Computing.mp4
Recommended video clip to view

## Slide 20: Vertical vs. horizontal load balancing
Vertically:
  More power, but centralized (one app. may run faster / more response / less latency for RT)
  Adding CPUs + memory to one system
  More dependent on one machine / group of closely coupled machines
Horizontally:
  More power, but wider distribution (more apps able to run at one time)
  Simpler scalability
  More distribution / redundancy / better risk management
…
MOPS
MOPS

## Slide 21: Step 8: Performance analysis
EEE4120F

## Slide 22: Performance analysis
Simple approaches involve using timers (i.e., as shown in previous code snippet)
  Usually quite straightforward for a serial situation or global memory
Monitoring and analyzing parallel programs can get a whole lot more challenging than for the serial case
  May add comms overhead
  Needing synchronization to avoid corrupting results, … could be a nontrivial algorithm itself

## Slide 23: MPI Timing functions
MPI_Wtime
  Returns the elapsed wall clock time in seconds (a double) on the calling processor
MPI_Wtick
  Returns the timer resolution in seconds (a double) of MPI_Wtime.
Note: MPI is the topic of a later lecture.
NB: MPI optional in 2023

## Slide 24: StdC: gettimeofday
gettimeofday
  Very portable, part of the StdC library
  Should be available on any Linux system
  Returns time in seconds and microseconds since midnight January 1 1970
  Uses struct timeval comprising
    tv_sec : number of seconds
    tv_usec : number of microseconds*
  Converting to microseconds will use huge numbers, rather work on differences
* Word of caution: some implementations always return 0 for the usec field!!
On Cygwin, the resolution is only in milliseconds, so tv_usec in multiples of 1000.
Not provided in DevC++.

## Slide 25: gettimeofday example
#include <stdio.h>
#include <sys/time.h>
#include <time.h>
struct timeval start_time, end_time; // variables to hold start and end time
int main() {
int tot_usecs;
int i,j,sum=0;
gettimeofday(&start_time, (struct timezone*)0); // starting timestamp
/* do some work */
for (i=0; i<10000; i++)
for (j=0; j<i; j++) sum += i*j;
gettimeofday(&end_time, (struct timezone*)0); // ending timestamp
tot_usecs = (end_time.tv_sec-start_time.tv_sec) * 1000000 +
(end_time.tv_usec-start_time.tv_usec);
printf("Total time: %d usec.\n", tot_usecs);
}
see timing.c code file
Provided previously

## Slide 26: Benchmarking
Process of measuring performance of DS
A program that Quantitatively evaluates computer Hardware and software resources
Benchmark suites – sets of benchmarks defined to get better system picture
Suitable benchmark for a system leads to an effective system

## Slide 27: Benchmarking (cont…)
What can be benchmarked? ( In DSP Compiler, Processor, Platform)
Compiler – Converts High Level Language to Assembly language thus we benchmark compiler efficiency
The Processor – code should be an Assembly (No more high level code)
Platform – Written in High Level language(Processor & Compiler)
(Recap mostly,
see earlier lecture)
Supplementary reading

## Slide 28: Benchmarking: what to measure
In DSP/HPEC systems we benchmark Cycle count, Data and Program memory usage, Execution time and Power consumption
What can we benchmark in Databases/Web servers (i.e Oracle, MySQL, SQL Server)?
SPEC defined several benchmarks in the digital world - SPECweb99, SPECmail, etc.
(This point mentioned already, next two are new…)
Supplementary reading

## Slide 29: Benchmark: Approaches
Metrics (MIPS, MOPS, MFLOPS, etc.) – some of these not really meaningful in RISC architectures (why?)
Complete DSP Application
  consumes time and effort as well as memory because it measure the whole system
DSP Algorithm Kernels
  extracted from real DSP programs and consist of small loops which perform number crunching, bit processing, etc.

## Slide 30: Benchmarking: Types
EEMBC (pron. embassy) – For embedded System and written in C
BDTIMARK – a DSP benchmark suite
Check this paper for a List of FPGA benchmarking types: Raphael Njuguna: A Survey of FPGA Benchmarks Available at: http://www.cse.wustl.edu/~jain/cse567-08/ftp/fpga.pdf) -- might be in exam
More Reading: Performance evaluation and Benchmarking, Lizy K. John and Lieven Eeckhout, Taylor & Francis Group
Supplementary reading

## Slide 31
Synchronization
Load balancing
Performance analysis and tuning
Part 2 Done
Over to you to work on OpenCL prac or have an early start on Prac3

## Slide 32: Questions?
?
?
?
?
?
?
?
?
?
?
?
?
?

## Slide 33: Further Reading / Refs
Suggestions for further reading, slides partially based / general principles elaborated in:
A Survey of FPGA Benchmarks Available at: http://www.cse.wustl.edu/~jain/cse567-08/ftp/fpga.pdf
Data dependencies suggested reading: http://sc.tamu.edu/help/power/powerlearn/html/ScalarOptnw/tsld036.htm
Load Balancing with Cloud Computing. https://www.youtube.com/watch?v=_xH5POea0Jc
FPGA benchmarking types: Raphael Njuguna: A Survey of FPGA Benchmarks Available at: http://www.cse.wustl.edu/~jain/cse567-08/ftp/fpga.pdf
“Performance evaluation and Benchmarking”, Lizy K. John and Lieven Eeckhout, Taylor & Francis Group

## Slide 34
Image sources:
Man running up stairs - Wikipedia (open commons)
Chocolate Chip Biscuit - Wikipedia (open commons)
Scales, Checked Flag - Open Clipart (http://openclipart.org)
Calendar Planning Image, Note pad – Pixabay (Public Domain CC0)
Yoga lady - adapted from Open Clipart
Disclaimers and copyright/licensing details
I have tried to follow the correct practices concerning copyright and licensing of material, particularly image sources that have been used in this presentation. I have put much effort into trying to make this material open access so that it can be of benefit to others in their teaching and learning practice. Any mistakes or omissions with regards to these issues I will correct when notified. To the best of my understanding the material in these slides can be shared according to the Creative Commons “Attribution-ShareAlike 4.0 International (CC BY-SA 4.0)” license, and that is why I selected that license to apply to this presentation (it’s not because I particulate want my slides referenced but more to acknowledge the sources and generosity of others who have provided free material such as the images I have used).

## Slide 35
Image sources:
Clipart sources – public domain CC0 (http://pixabay.com/)
PxFuel – CC0 (https://www.pxfuel.com/)
Pixabay
commons.wikimedia.org
Images from flickr
Disclaimers and copyright/licensing details
I have tried to follow the correct practices concerning copyright and licensing of material, particularly image sources that have been used in this presentation. I have put much effort into trying to make this material open access so that it can be of benefit to others in their teaching and learning practice. Any mistakes or omissions with regards to these issues I will correct when notified. To the best of my understanding the material in these slides can be shared according to the Creative Commons “Attribution-ShareAlike 4.0 International (CC BY-SA 4.0)” license, and that is why I selected that license to apply to this presentation (it’s not because I particulate want my slides referenced but more to acknowledge the sources and generosity of others who have provided free material such as the images I have used).